## Slide 1: Residual Deep O Net Applied to Molecular Dynamics Simulation of Polymer Diodes
Isaac Smith
Mar 18 2026

## Slide 2: Polymer Diodes
Flexible LEDs
Brain-computer interfaces
Sensing applications
  Light
  pH
  And more..
Zhen et al. 2017. Full-solution processed, flexible, top-emitting polymer light-emitting diodes based on printed Ag electrodes.

## Slide 3: Our System
Mobile ions moving in a polyion matrix
We want to model the current as a function of applied electric voltage
Mobile Cations, Fixed Polyanions
Mobile Anions, Fixed Polycations
-
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-

## Slide 4: How can we model this system?
Molecular dynamics?
  Possible, but expensive
Analytics/Continuum?
  Misses excluded volume effects
  Analytics are difficult for more complex geometry

## Slide 5: How can we model this system?
We want to model current as a function of applied electric field

## Slide 6: How can we model this system?
We want to model current as a function of applied electric field

## Slide 7: How can we model this system?
We want to model current as a function of applied electric field
Ohm’s law:
But this system is not purely resistive

## Slide 8: Residual Neural Operator
Model the difference between true behavior and Ohm’s law:
Use a deep O net for the residual
E(t)
Branch Net
t_i
Trunk Net
R(t_i)
Dot Product

## Slide 9: Residual Neural Operator
E(t)
Branch Net (801, 256)->Tanh->(256, 256)->Tanh->(256 256)
t_i
Trunk Net (1, 64)->Tanh->(64, 64)->Tanh->(64, 256)
R(t_i)
Dot Product

## Slide 10: Residual Neural Operator
Deep O nets can deal with unequally spaced data
Not a problem for this case, but useful versatility
E(t)
Branch Net
t_i
Trunk Net
R(t_i)
Dot Product

## Slide 11: Data Generation
Data generated by molecular dynamics
100 electric field functions with random parameters
  Mix of polynomial and sinusoidal components

## Slide 12: Molecular Dynamics
Many dimensional ODE integrator
Each particle experiences a force based on the state of the system at that timestep

## Slide 13: Training
Use spline smoothed data
30000 cycles, each with one randomly chosen point
Decreasing learning rate

## Slide 14: Model Performance
On the test data set:
  Mean loss per trajectory: 29.65
  Standard Deviation: 11.07

## Slide 15: Model Performance

## Slide 16: Discussion
Better than Ohm’s law
Spectral bias is a large issue
Different architectures might do better
  FNO

## Slide 17: Thank you!